crack segmentation tool

---
feature
- paint brush
  - paint on crack area
  - clean the painted mask area
  - adjust paint radius
- Segmentation
  - opencv Grabcut
  - Canny edge

---
grab-cut
- Just works when the surrounding area is different from crack area
- Fail when crack is small and looks similar to the background (pavement)

---
Canny edge

---
Canny edge
- Threshold calculation
  - Median of all gray pixels in the painted area
  - Lower: median – 0.3
  - Upper: median + 0.3
- Problems
  - Lot of noise
  - Missing crack lines

---
Next step
- segmentation
  - Cut the painted area into smaller segments?
    - Calculate canny edge threshold per segment
  - Tried different adaptive threshold method?
  - Other idea?